## Slide 1
Fluid Mechanics
CE 261

## Slide 2
Ser | Topic | Remarks
1 | Development and Scope of Fluid Mechanics | Lt Col Zakir
2 | Fluid Properties | Lt Col Zakir
3 | Fluid Statics | Lt Col Zakir
4 | Kinematics of Fluid Flow | 
5 | Fluid Flow Concepts and Basic Equations: Continuity Equation, Bernoulli’s Equation, Energy Equation, Momentum Equation, Forces in Fluid Flow | 
6 | Similitude and Dimensional Analysis | Lt Col Zakir
7 | Steady Incompressible Flow in Pressure Conduits | 
8 | Laminar and Turbulent Flow | 
9 | General Equation for Fluid Friction | 
10 | Empirical Equation for Pipe Flow | 
11 | Minor Losses in Pipe Flow | 
12 | Fluid Measurement: Pitot Tube, Orifice, Mouthpiece, Nozzle, Venturimeter, Weir | Lt Col Zakir
13 | Pipe Flow Problems: Pipes in Series and Parallel, Branching Pipes Pipe Networks | 
Syllabus

## Slide 3
Primary Text Book:
Fluid Mechanics with Engineering Applications
By Robery L. Daugherty, Josheph B. Franzini and E. JohnFinnemore
References:
Fluid Mechanics, V.L. Streeter
Hydraulics, H.W. King
Hydraulics and Fluid Mechanics, E.W. Lewit
Elementary Fluid Mechanics. J. K. Vernerd, R. L. Srteet
Introduction to Fluid Mechanics, R. W. Fax, A. T. Mc Donald
Mechanics of Fluid, I. H. Shames

## Slide 4: Chapter 1 Properties of Fluid

## Slide 5: Introduction
Fluid mechanics is a study of the behavior of fluids, either at rest (fluid statics) or in motion (fluid dynamics).
The analysis is based on the fundamental laws of mechanics, which relate continuity of mass and energy with force and momentum.
An understanding of the properties and behavior of fluids at rest and in motion is of great importance in engineering.

## Slide 6: Lesson Objectives
Identify the units for the basic quantities of time, length, force and mass.
Properly set up equations to ensure consistency of units.
Define and understand the basic fluid properties.
Identify the relationships between specific weight, specific gravity and density, and solve problems using their relationships.

## Slide 7
Development of Fluid Mechanics
Fluid Mechanics Divided in to three branches:
Fluid Statics:
Fluid Kinematics:
Fluid Dynamics:
Hydrodymamics Hydraulics
Fluid Mechanics

## Slide 8: 1.1 Definition of Fluid
A fluid is a substance, which deforms continuously, or flows, when subjected to shearing force
In fact if a shear stress is acting on a fluid it will flow and if a fluid is at rest there is no shear stress acting on it.
Fluid Flow
Shear stress – Yes
Fluid Rest
Shear stress – No

## Slide 9: Shear stress in moving fluid
If fluid is in motion, shear stresses are developed if the particles of the fluid move relative to each other. Adjacent particles have different velocities, causing the shape of the fluid to become distorted
On the other hand, if the velocity of the fluid is the same at every point, no shear stress will be produced, the fluid particles are at rest relative to each other.
Moving plate
Shear force
Fluid particles
New particle position
Fixed surface

## Slide 10: 1.1 Distinction Between Solid and Fluid
Molecules of a solid are closer together than those of a fluid. A fluid is a substance, which deforms continuously, or flows, when subjected to shearing force
The attractive forces between molecules of a solid are so large that solid tends to retain its shape. But in case of fluid attractive forces between molecules are smaller.
Fluid will yield to slighest stress no matter how viscous it is. But solid require some magnitude of stress.
Solid tend to restore its original shape after removal of external forces.

## Slide 11: Differences between liquid and gases
Liquid | Gases
Difficult to compress and often regarded as incompressible | Easily to compress – changes of volume is large, cannot normally be neglected and are related to temperature
Occupies a fixed volume and will take the shape of the container | No fixed volume, it changes volume to expand to fill the containing vessels
A free surface is formed if the volume of container is greater than the liquid. | Completely fill the vessel so that no free surface is formed.

## Slide 12: 1.3 Fluid Properties
Density
Density of a fluid, ,
Definition: mass per unit volume,
slightly affected by changes in temperature and pressure.
 = mass/volume = m/v (1.2)
Units: kg/m3
Typical values:
Water = 1000 kg/m3; Air = 1.23 kg/m3

## Slide 13: Fluid Properties (Continue)
Specific weight
Specific weight of a fluid, 
Definition: weight of the fluid per unit volume
Arising from the existence of a gravitational force
The relationship  and g can be found using the following:
Since  = m/
therefore  = g (1.3)
Units: N/m3
Typical values:
Water = 9814 N/m3; Air = 12.07 N/m3

## Slide 14: Fluid Properties (Continue)
Specific Volume
Specific weight of a fluid, v
Definition: Volume occupied by unit mass of fluid
Commonly implied to gases
The relationship  and g can be found using the following:
Since  = 1/v
Units: m3 / kg

## Slide 15: Fluid Properties (Continue)
Specific gravity
The specific gravity (or relative density) can be defined in two ways:
  Definition 1: A ratio of the density of a substance to the density of water at standard temperature (4C) and atmospheric pressure, or
  Definition 2: A ratio of the specific weight of a substance to the specific weight of water at standard temperature (4C) and atmospheric pressure.
(1.4)
Unit: dimensionless.

## Slide 16: Fluid Properties (Continue)
Viscosity
Viscosity, , is the property of a fluid, due to cohesion and interaction between molecules, which offers resistance to shear deformation.
Different fluids deform at different rates under the same shear stress. The ease with which a fluid pours in is an indication of its viscosity. Fluid with a high viscosity such as syrup deforms more slowly than fluid with a low viscosity such as water. The viscosity is also known as dynamic viscosity.
Units: N.s/m2 or kg/m/s
Typical values:
Water = 1.14x10-3 kg/m/s; Air = 1.78x10-5 kg/m/s

## Slide 17
Kinematic viscosity, 
Definition: is the ratio of the viscosity to the density;
will be found to be important in cases in which significant viscous and gravitational forces exist.
Units: m2/s
Typical values:
Water = 1.14x10-6 m2/s; Air = 1.46x10-5 m2/s;
In general,
viscosity of liquids with temperature, whereas
viscosity of gases with in temperature.

## Slide 18: Newtonian and Non-Newtonian Fluid
Example:
Air
Water
Oil
Gasoline
Alcohol
Kerosene
Benzene
Glycerine
Fluid
Newton’s law
of viscosity
Newtonian fluids
obey
refer
Newton’s’ law of viscosity is given by;
(1.1)
The viscosity  is a function only of the condition of the fluid, particularly its temperature.
The magnitude of the velocity gradient (du/dy) has no effect on the magnitude of .
 = shear stress
 = viscosity of fluid
du/dy = shear rate, rate of strain or velocity gradient

## Slide 19: Newtonian and Non-Newtonian Fluid
Fluid
Newton’s law
of viscosity
Non- Newtonian
fluids
Do not obey
The viscosity of the non-Newtonian fluid is dependent on the velocity gradient as well as the condition of the fluid.
Newtonian Fluids
a linear relationship between shear stress and the velocity gradient (rate of shear),
the slope is constant
the viscosity is constant
non-Newtonian fluids
slope of the curves for non-Newtonian fluids varies

## Slide 20
Figure 1.1
Shear stress vs. velocity gradient
Bingham plastic : resist a small shear stress but flow easily under large shear stresses, e.g. sewage sludge, toothpaste, and jellies.
Pseudo plastic : most non-Newtonian fluids fall under this group. Viscosity decreases with increasing velocity gradient, e.g. colloidal substances like clay, milk, and cement.
Dilatants : viscosity decreases with increasing velocity gradient, e.g. quicksand.

## Slide 21: 1.2 Engineering Units
Primary Units
In fluid mechanics we are generally only interested in the top four units from this table.
Quantity | SI Unit
Length | Metre, m
Mass | Kilogram, kg
Time | Seconds, s
Temperature | Kelvin, K
Current | Ampere, A
Luminosity | Candela

## Slide 22
Derived Units
Quantity | SI Unit | 
velocity | m/s | -
acceleration | m/s2 | -
force | Newton (N) | N = kg.m/s2
energy (or work) | Joule (J) | J = N.m = kg.m2/s2
power | Watt (W) | W = N.m/s = kg.m2/s3
pressure (or stress) | Pascal (P) | P = N/m2 = kg/m/s2
density | kg/m3 | -
specific weight | N/m3 = kg/m2/s2 | N/m3 = kg/m2/s2
relative density | a ratio (no units) | dimensionless
viscosity | N.s/m2 | N.s/m2 = kg/m/s
surface tension | N/m | N/m = kg/s2

## Slide 23: Bulk Modulus or Volume Modulus of Elasticity
All fluids are compressible under the application of an external force and when the force is removed they expand back to their original volume.
The compressibility of a fluid is expressed by its bulk modulus of elasticity, K, which describes the variation of volume with change of pressure, i.e.
Thus, if the pressure intensity of a volume of fluid, , is increased by Δp and the volume is changed by Δ, then
Typical values:Water = 2.05x109 N/m2; Oil = 1.62x109 N/m2

## Slide 24: Vapor Pressure
A liquid in a closed container is subjected to a partial vapor pressure in the space above the liquid due to the escaping molecules from the surface;
It reaches a stage of equilibrium when this pressure reaches saturated vapor pressure.
Since this depends upon molecular activity, which is a function of temperature, the vapor pressure of a fluid also depends on its temperature and increases with it.
If the pressure above a liquid reaches the vapor pressure of the liquid, boiling occurs; for example if the pressure is reduced sufficiently boiling may occur at room temperature.

## Slide 25: Engineering significance of vapor pressure
In a closed hydraulic system, Ex. in pipelines or pumps, water vaporizes rapidly in regions where the pressure drops below the vapor pressure.
There will be local boiling and a cloud of vapor bubbles will form.
This phenomenon is known as cavitations, and can cause serious problems, since the flow of fluid can sweep this cloud of bubbles on into an area of higher pressure where the bubbles will collapse suddenly.
If this should occur in contact with a solid surface, very serious damage can result due to the very large force with which the liquid hits the surface.
Cavitations can affect the performance of hydraulic machinery such as pumps, turbines and propellers, and the impact of collapsing bubbles can cause local erosion of metal surface.
Cavitations in a closed hydraulic system can be avoided by maintaining the pressure above the vapor pressure everywhere in the system.

## Slide 26: Surface Tension
Liquids possess the properties of cohesion and adhesion due to molecular attraction.
Due to the property of cohesion, liquids can resist small tensile forces at the interface between the liquid and air, known as surface tension, .
Surface tension is defined as force per unit length, and its unit is N/m.
The reason for the existence of this force arises from intermolecular attraction. In the body of the liquid (Fig. 1.2a), a molecule is surrounded by other molecules and intermolecular forces are symmetrical and in equilibrium.
At the surface of the liquid (Fig. 1.2b), a molecule has this force acting only through 180.
This imbalance forces means that the molecules at the surface tend to be drawn together, and they act rather like a very thin membrane under tension.
This causes a slight deformation at the surface of the liquid (the meniscus effect).
Figure 1.2: Surface Tension

## Slide 27
A steel needle floating on water, the spherical shape of dewdrops, and the rise or fall of liquid in capillary tubes is the results of the surface tension.
Surface tension is usually very small compared with other forces in fluid flows (e.g. surface tension for water at 20C is 0.0728 N/m).
(1.7)

## Slide 28: Capillarity
The surface tension leads to the phenomenon known as capillarity
where a column of liquid in a tube is supported in the absence of an externally applied pressure.
Rise or fall of a liquid in a capillary tube is caused by surface tension and depends on the relative magnitude of cohesion of the liquid and the adhesion of the liquid to the walls of the containing vessels.
Liquid rise in tubes if they wet a surface (adhesion > cohesion), such as water, and fall in tubes that do not wet (cohesion > adhesion), such as mercury.
Capillarity is important when using tubes smaller than 10 mm (3/8 in.).
For tube larger than 12 mm (1/2 in.) capillarity effects are negligible.

## Slide 29
Figure 1.3 Capillary actions
(1.8)
where h = height of capillary rise (or depression)
 = surface tension
 = wetting (contact) angle
 = specific weight of liquid
r = radius of tube

## Slide 30
Thank You