## Slide 1
Fluid Statics
In fluids at rest there are no shear stresses;
only normal forces due to pressure are present.
Normal forces produced by static fluids are often very important.
-For example,
they tend to overturn concrete dams,
burst pressure vessels,
and break lock gates on canals.
Obviously, to design such facilities, we need to be able to compute the magnitudes and locations of normal pressure forces. Understanding them, we can also develop instruments to measure pres sures, and systems that transfer pressures, such as for automobile brakes and hoists.

## Slide 2: Fluid Statics
The average pressure intensity p is the force exerted on a unit area. If F represents the total normal pressure force on some finite area A, while dF represents the force on an infinitesimal area dA, the pressure is
p= dF/dA
if the pressure is uniform over the total area, then
p = F/A.
Units
  psi(lb/in2)
  psf(lb/ft2
  Pa(N/m2) or
  kPa (kN/m2).

## Slide 3: Fluid Statics
PRESSURE AT A POINT THE SAME IN ALL DIRECTIONS
Reasons:
no tangential stresses can exist in a fluid at rest
only forces between adjacent surfaces are pressure forces normal to the surfaces.
Proof:
a very small wedge-shaped element of fluid at rest whose thickness perpendicular to the

## Slide 4: Fluid Statics
Proof:
a very small wedge-shaped element of fluid at rest whose thickness perpendicular to the plane of the paper is dy. Let p be the average pressure in any direction and let px and pz be the average pressures in the horizontal and vertical directions. forces in the y direction cancel each other. For equilibrium, the sum of the force components on the element in any direction must be equal to zero. in the x di­rection,
pdldycosα - pxdydz = 0.
Since dz = dlcosa,
it follows that p = px.
Similarly, in the z direction gives
pZ dx dy - p dl dy sin α – 1/2 ϒ dx dy dz = 0.
The third term is of higher order than the other two terms and so may be neglected. It follows from this that p = pZ. We can also prove that p = py by considering a three-dimensional case. The results are independent of α; thus the pressure at any point in a fluid at rest is the same in all directions.

## Slide 5: Fluid Statics
VARIATION OF PRESSURE IN A STATIC FLUID
Consider the differential element (or control volume) of
static fluid shown in Fig. pressure at the center p.
The forces acting in the vertical direction are (a)
The body force, the action of gravity on the mass within
the element, and (b) the surface forces, transmitted
from the surrounding fluid and acting at right angles
against the top, bottom, and sides of the element.
summation of forces acting on the element in any
direction must be zero. If forces are summed in the
horizontal direction, that is, x or y, the only forces acting
are the pressure forces on the vertical faces of the
element. To satisfy
and
the pressures on the opposite vertical faces must be equal. Thus for the case of the fluid at rest.

## Slide 6: Fluid Statics
Summing forces in the vertical direction and setting the sum equal to zero,
This results in
since p is independent of x and y, this can be written as (3.2)
This is the general expression that relates variation of pressure in a static fluid to vertical
position. The minus sign indicates that as z gets larger (increasing ele­vation), the
pressure gets smaller.
To evaluate the pressure anywhere in a fluid at rest, we must integrate Eqn 3.2 between
appropriately chosen limits. For incompressible fluids (ϒ = constant), we can integrate Eq.
(3.2) directly.
For compressible fluids, however, we must express y algebraically as a function of z or p
if we wish to determine pressure accurately as a function of elevation
(3.3)

## Slide 7: Fluid Statics
PRESSURE EXPRESSED IN HEIGHT OF FLUID
Imagine an open tank of liquid with no pressure acting on its surface (Fig. 3.3), though in reality the minimum pressure upon any liquid surface is the pressure of its own vapor. Disregarding this for the moment, by Eq. (3.4), the pressure at any depth h is p = yh. If we assume y to be constant, there is a definite relation between p and h. That is, pressure (i.e., force per unit area) is equivalent to a height h of some fluid of constant specific weight y. Often we find it more con­venient to express pressure in terms of a height of a column of fluid rather than in pressure per unit area.
Even if the surface of the liquid is under some pressure, we only need to convert this pressure into an equivalent height of the fluid in question and add this to the value of h shown in Fig. 3.3, to obtain the total pressure.
Thus we may relate pressure p to the height of a column of any fluid by the expression
This relationship is true for any consistent system of units. When we express pressure in this way, in terms of a height of fluid, we commonly refer to it as pres­sure head

## Slide 8: Fluid Statics
An important property follows from Eq. (3.3), which we can express as:
For Incompressible fluid:
p/ϒ + z = p1 /ϒ + z1 = constant
This shows that for an incompressible fluid at rest, at any point in the fluid the sum of the elevation z and the pressure head p/ϒ is equal to the sum of these two quantities at any other point. The significance of this statement is that, in a fluid at rest, with an increase in elevation there is a decrease in pressure head, and vice versa. This concept is depicted in Fig.

## Slide 9: Fluid Statics
pressure relative to absolute zero is called absolute pressure; Pressure relative to atmospheric pressure is gage pressure.
If the pressure is below that of the atmosphere, we call it a vacuum.
All values of absolute pressure are positive,
We can see from the preceding discussion that the following relation holds,
pabs = Patm + Pgage
where pgage may be positive or negative (vacuum).

## Slide 10: Fluid Statics Measurement of Pressure
Barometer
We measure the absolute pressure of the atmosphere with a barometer.
From the concepts developed in Sec. 3.2, we see that the pressure at 0, po = pa = patm. But, from Eq. (3.4) and Sec. 3.2,
po = ϒy + pvapor
Because of the static equilibrium, we may equate the pressures at 0 to obtain
patm = ϒy + Pvapor (3.8)
If the vapor pressure on the surface of the liquid in the tube were negligible, then we would have
Patm = ϒy
Mercury is used to keep the tube short.

## Slide 11: Fluid Statics Measurement of Pressure
Bourdon Gage
We commonly measure pressures or vacuums with the Bourdon gage.
When a pressure and vacuum gage is combined into one we call this a compound gage.
The pressure indicated by such gages is that at their centers. If the connecting piping is filled completely with fluid of the same density and if the pressure gage is graduated to read in pounds per square inch, as is customary, then
pA(psi) = gage reading (psi) + ϒh/144

## Slide 12: Fluid Statics
Pressure Transducer
A transducer is a device that transfers energy (in any form) from one system to another.
A Bourdon gage is a mechanical transducer
An electrical pressure transducer converts the displacement of a mechanical system (usually a metal diaphragm) to an electric signal, either actively if it generates its own electrical output or passively if it requires an electrical input that it modifies as a function of the me­chanical displacement.
As the pressure changes, the deflection of the diaphragm changes. This, in turn, changes the electrical output, which, through proper calibration, can provide pressure.
If we connect such a device to a strip-chart recorder we can use it to give a continuous record of pressure

## Slide 13: Fluid Statics Measurement of Pressure
Piezometer Column
A piezometer column is a simple device for measuring moderate pressures of liquids.
It consists of a sufficiently long tube in which the liquid can freely rise without overflowing.
The height of the liquid in the tube will give the value of the pressure head, p/ϒ directly.
To reduce capillary error the tube diameter should be at least 0.5 in (12 mm).
open piezometer tube is too tall and cumbersome for use with liquids under high pressure and gases

## Slide 14: Fluid Statics Measurement of Pressure
Simple Manometer
simple manometer or mercury U tube is a convenient device for measuring many pressures.
Let sM be the specific gravity of the manometer fluid and sF as the specific gravity of the fluid whose pressure is being measured. let us identify a manometer reading by Rm; in Fig this is the height OC. If y' is the height of a column of measured fluid that would exert the same pressure at C as does the column of manometer fluid OC, height Rm
gage pressure pc = ϒMRm = ϒF y'
and by rearranging
y‘ = (ϒM / ϒF) Rm = (pM / pF )Rm =(SM / SF) Rm
Thus the gage pressure at C, in terms of the fluid whose pressure we are mea­suring, as required, is ϒ(SM / SF) Rm This is also the pressure at B because the fluid in BC is in balance. The pressure at A is
0 + ϒ(SM / SF) Rm + ϒh = PA
Or divide all terms by ϒ to get the pressure head